PROPOSED INSTALLATION OF ROAD HUMPS, MIDLOTHIAN

Easter Langside Gardens, Dalkeith.

The Council proposes to install four road humps on Oak Crescent, Mayfield, Dalkeith:, one each at approximately 85m, 155m, 260m and 320m from Bogwood Road.

This proposal is in response to concerns about speeds of vehicles and difficulty for pedestrians and cyclists using the road, with injury accidents reported.

The humps would be sinsusoidal in profile, a maximum of 75mm high, 3.7m long and have tapered edges (i.e. small gaps between the hump and the kerbs at each side of the road) for drainage.

January 2019.